## Slide 1
Geology 5660/6660
Applied Geophysics
1 Mar 2024
© A.R. Lowry 2008-2024
Read for Mon 4 Mar: Burger 524-539 (§8.4)
Last Time: Seismic Reflection Interpretation
• 4D seismic: Multiple 3D reflection images over time aid in
optimization of reservoir models and production
• Salt structures are especially challenging but have been a
focus of innovation
• EM imaging is a tool of growing importance; electrical
resistivity is sensitive to fluids and clay content
• Knowledge of geological processes is key to
interpretation!!!! BUT, it’s critically important to
also understand attributes/artefacts/limitations
of the seismic reflection data.

## Slide 2
Ground Penetrating Radar:
Radar  electromagnetic waves (light) at radio frequencies
(50 to 1000 MHz).
Governed by physics of the wave equation (so in some
respects it is very similar to seismic methods: V = f!)
Requires a source and receiver (dipole antennae for both)
Source transmits a single pulse:
but can transmit and receive millions of pulses per second!
0
5x10-9 s
Amplitude
time
Power
frequency
10 Mhz
100
1000

## Slide 3
Display is very similar to seismic: Amplitude (voltage)
versus time on a “trace”. Source-receiver is usually
zero-offset (but can use NMO profiling, CMP gathers)
High frequency  requires high sampling rate, very
precise electronics
Lots more source/receiver obs  lots of stacking of
reflection energy; denser spatial sampling
Higher frequency  higher resolution
High attenuation  very shallow (< a few 10s of m)
Two-way travel time (µs)
(Like seismic,
convention is blue = positive, red = negative impedance contrast!

## Slide 4
Like seismic, waves are reflected & transmitted at interfaces
with differing impedance properties:
layer 1
layer 2
E0
E1
E2
Snell’s law applies
Amplitude dependence is different
(simpler) because there is only one
type of wave.
Reflection R & Transmission T
coefficients are similar to
seismic at 90°angle of incidence:
where Zi is the electromagnetic impedance in layer i,
but no converted waves (so no Zoeppritz’ equations!)

## Slide 5
Recall for seismic: Acoustic Impedance Zi = iVi
For Electromagnetic Impedance,
where:  = circular frequency (2pf )
 = absolute permittivity (real-valued)
 = relative magnetic permeability
 = electrical resistivity
 = 1/ = electrical conductivity
r is called the “relative dielectric permittivity”
and is a complex variable!
All of these parameters (except frequency ) are physical
properties of the medium, so like impedance & velocity
in seismic studies, these contain information about
properties of the targeted volume!
The real part of er defines propagation; the imaginary part defines attenuation!

## Slide 6
Most modern radar sections are converted from two-way
travel-time to depth using an assumed value for velocity…
The true velocity is

## Slide 7
Soil and Rock Properties:
Relative Magnetic Permeability
 ~ 1 for most rocks;
1.05 for hematite
5 for magnetite
Relative dielectric permittivity r has ~ real part:
(dry) (wet)
(defined as: )
magnetic flux density
magnetic field intensity
4
30
soil
3
30
sand
5
12
sandstone
7
40
clay
water
80
88
(fresh)
(brine)
4
8
limestone
5
15
shale

## Slide 8
For most applications (i.e., shallow near-surface)
1 ≈ 2 ≈ 1;  (10-4–10-1) « (106–1010!), and hence
(i.e., we are imaging velocity variations corresponding to
changes in relative dielectric permittivity!)
For the water table, R ~ 0.1
Recall seismic waves attenuate as where Q
is quality factor;
Radar waves attenuate similarly as ; where
Attenuation is extremely high for shale, silt, clay, and
briny water (which is why GPR rarely penetrates > 10 m!).
