## Slide 1
Geology 5660/6660
Applied Geophysics
2 Feb 2024
© A.R. Lowry 2008-2024
Read for Mon 5 Feb: Burger 106-141 (§3.7-3.11)
Last time: Zoeppritz’ equations and AVO
• Zoeppritz’ equations give amplitudes of reflections and
refractions that vary with angle of incidence at a boundary
• Amplitude vs offset (AVO) uses reflection amplitudes
at different offsets (hence different i0) to infer properties
The Refraction Method:
• For a single horizontal layer over a halfspace,
observed travel-times for direct and refracted arrivals:
give the velocities and layer thickness from t = mi x + bi as:

## Slide 2
V1
Direct arrival
Refracted arrival
a
b
ic
h
V2
Practical note: This works for a horizontal interface, and then
only if there are enough geophones before & after the
crossover distance xco (where arrival times for the direct
& refracted arrival are the
same) to solve for
equations of the two
lines:
or
xco
xco

## Slide 3
Spatial sampling is key to getting accurate estimates
of thickness: Must have multiple geophones that sample
each layer. Since we don’t know the structure when
designing the experiment, this means lots of closely-
spaced geophones… Where “close” is determined by
minimum expected thickness and maximum expected
velocity difference!

## Slide 4
V1
Direct arrival
Refracted arrival
a
b = xc/2
ic
h
V2
Another term that crops up in refraction studies is the
critical distance = the horizontal distance traveled in
layer 1 by the ray having critical angle ic (i.e., xc = 2b).
In situations where we have some approximate idea of the
range of thicknesses & velocities we might expect to find,
calculating the crossover and critical distances inform
experiment design (i.e., how many geophones to use,
offset & spacing).

## Slide 5
V1
Direct arrival
i1
h1
V2
V3
h2
Refracted arrival
For multiple layers we take advantage of Snell’s Law:
Via similar algebra & geometry to the one-layer case,
or, generalizing to n-layers:

## Slide 6
Recall that your 2nd lab assignment asks for two crossover
distances (between the direct arrival and the first refraction,
and between the first refraction and the second refraction). We’ve
already derived the equation for the first of these, and the
equation for the second can be found similarly: We require that
If we recall that these are the equations of lines with slopes (m2, m3)
and intercepts (b2, b3), a simplified way to write the solution is:
1

## Slide 7
V1
Direct arrival
Refracted arrival
ic
h
V2
?

## Slide 8
V1
Direct arrival
Refracted arrival
ic
hu
V2
Refraction from a dipping
interface:
Now thickness changes with
offset, so slope is no longer
= inverse of layer velocity.
Refer to as “apparent
velocity ”, and this is why
we reverse our shots!
hd

After some trig & algebra, we get:
tdd
tud
md
mu
t0d
t0u

## Slide 9
Like before, we have the observed travel-times and want to
know the model parameters. We know V1 from the direct
arrival, & we can show that the slopes are:
then we can solve for velocity V2:

and angle :
The normal thicknesses use intercept times t0u, t0d:
(Can get vertical distance from shot to top of layer by dividing
hd or hu by cos ).