## Slide 1
Geology 5660/6660
Applied Geophysics
8 Apr 2026
© A.R. Lowry 2008-2026
For Fri 10 Apr: Burger 265-301 (§5.1-5.4)
Last Time: Magnetic Modeling
• Induced magnetic field due to a dipole is given by:
• Magnetic field for an arbitrarily-shaped body is:
• Often we use analytical solutions derived for simple
body shapes, e.g., for a sphere of radius R:
• Semi-infinite sheet:
• GravMag uses Talwani solutions for 2D prisms…

## Slide 2
Last Time continued: Intro to DC Electrical Resistivity
• DC Resistivity : inject electrical current across two (source
& sink) electrodes, measure voltage across two others.
• Governing equation derives from Maxwell’s equations…
to get Ohm’s Law :

## Slide 3
DC Electrical Resistivity
Source
Sink
i
Current (charge) flow
Electrical
equipotential
Ohm’s Law:
So for a given current i and electrode
spacing d (defines ), V depends on 
d
+
–
V

## Slide 4
1
10
1000
104
105
106
100
Resistivity ( m)
clay
topsoil
shale
porous limestone
dense limestone
metamorphic rocks
igneous rocks
graphitic schist
gravel
weathered bedrock
gabbro
sandstone
Resistivity properties of rocks & soils:

## Slide 5
Sulfides
Temperature
Water Salinity in
Pore Fluids

## Slide 6
Example: Current source I in an infinite homogeneous
medium with constant resistivity 
Expect V = 0 at r =  and equipotential
surfaces are spherical around the source
(similar to gravity!)
(for some unknown constant A)
so
Integrating the relation above, then
or equivalently
So given a known I & a measured voltage at known r,
we can solve for a constant resistivity .
+

## Slide 7
More realistic representation of Earth is a halfspace:
Same current is forced into half the volume so
or equivalently
And for two current electrodes +I and –I, total potential
is given by the sum of potentials from the two
point sources:
r1
r2
V
+
+
–

## Slide 8
In practice we measure voltage difference at two points,
V = Va – Vb
1
2
a
b

## Slide 9
We are really interested however in imaging a subsurface
in which r varies. The potentials integrate  over the
volume so they provide information relevant for doing
exactly that!

## Slide 10
Electrode Arrays: Spatial placement of the electrodes
Wenner Array: (common in older surveys)
I
a
Constant spacing (“a-spacing”):
r1a = r2b = a r1b = r2a = 2a
a
a
V

## Slide 11
Wenner-Lee Array:
I
a
Additional voltage measurements to a center electrode
reduce sensitivity to near-surface resistivity variations
a
a
I
2s
a
Schlumberger Array:
Also less sensitive to near-surface resistivity variations,
& required half the effort to move electrodes for
sounding studies (of vertical changes in resistivity)
V1
V2
V3
V

## Slide 12
Dipole-Dipole Array:
I
Requires larger current source, but fairly common now
with the development of multichannel instruments
Pole-Dipole Array:
Most sensitive to resistivity in the shell between radii
r1 & r2 – commonly used for tunnel/karst detection
I
r1
r2
V
V

## Slide 13
Modeling:
Current penetration for a layer over half-space:
Fraction of total current that penetrates below depth
of an interface, z, is (for a Wenner array):
2
1
a is electrode spacing,

## Slide 14
2
1
z = a
z = 3a/2
z = 3a
k = 0.67; z = a/2
k = –0.67; z = a/2

## Slide 15
Apparent resistivity for a layer over halfspace: For Wenner
array, given by:
Sounding increases the a-spacing without changing the array center, to reflect larger volumes and hence deeper structure!

## Slide 16
Apparent resistivity for the two-layer over half-space case:
for various half-space resistivity values.

## Slide 17
Dependence of apparent resistivity on thickness of middle layer
Apparent resistivity for the two-layer over halfspace case:

## Slide 18
“Universal Curves"
Wenner array app depends only on 2/1, a/d1 for layer over a
halfspace

## Slide 19
For 3+ layers:
Rule of thumb: if layer thickness < 0.1 the depth to top of
layer, it cannot be resolved
But also depends on resistivity contrast (thicker layers may
not be resolved if contrast is too small; transition of
apparent resistivity versus a-spacing is much sharper for
a resistive layer over a conductive layer than for the
opposite).
When layer thickness is small relative to depth-to-top,
solution from sounding can be highly non-unique

## Slide 20
Resist does either Wenner or Schlumberger array for
vertical sounding only (horizontal layers); and is
somewhat less adaptable than the other Burger programs
 = 100  m
 = 10  m
 = 500  m
 = 10000  m
10 m
10 m
10 m
(Particularly because of
forced logarithmic
variation of a-spacing)
(Worth noting though that the Burger Excel spreadsheets are much more flexible & adaptable!

## Slide 21
Profiling maintains constant a-spacing while moving the
array laterally. Wenner array app for a vertical contact:
 = 100  m
 = 10  m
I
V

## Slide 22
Sounding maintains a constant center while increasing
the a-spacing. Wenner array app for a vertical contact:
 = 100  m
 = 10  m
x
I
V

## Slide 23
“Sensitivity kernels”
for apparent
resistivity (assumes
a homogeneous
Earth model). This is
a measure of how
much a perturbation
of resistivity at a given
point in the Earth can
be expected to change
the measurement of
apparent resistivity of
the array (reds positive,
blue-greens negative,
yellow ~ zero).