## Slide 1
Geology 5660/6660
Applied Geophysics
10 Apr 2026
© A.R. Lowry 2008-2026
Last Time: Intro to DC Electrical Resistivity
• DC Resistivity: inject electrical current across two (source & sink)
electrodes, measure voltage across two others.
• Material property imaged is rock resistivity:
 Low for clays, shales, graphite; intermediate for soils/unconsolidated
sediments; high for consolidated sediments and crystalline rocks
 Sensitive to sulfides, temperature, pore fluids
• Given known distances r between current electrodes
(+ = 1, – = 2) and voltage measurement electrodes
(+ = a, – = b) and a known injection current I, the
apparent resistivity rapp:
is an expression of the measurement that assumes the
medium has constant resistivity r (but in reality it is a “weighted
average” of the subsurface resistivity).
For Mon 13 Apr: Burger 302-340 (§5.5-5.11)

## Slide 2
Last Time continued: DC Electrical Resistivity
• Electrode Arrays:
 Wenner (constant spacing):
 Wenner-Lee (local voltage measurements)
 Schlumberger (move only current
electrodes):
 Dipole-dipole
 Pole-dipole (simple approach for tunnels/karst)
• In a layered medium, current penetration into a
second layer depends on depth of the layer interface
& resistivities as:
where

## Slide 3
Last Time continued: DC Electrical Resistivity
• One-Dimensional Sounding:
 Layer-over-halfspace: Wenner app ~  for a/z small;
~ 2 for a/z large
 Two layers over halfspace: May or may not pick up
sandwiched layer depending on thickness, contrast
 Resist does multiple layers, 1D, log a-spacing steps
• Profiling: Vertical contact: app depends on where resistivity
contrasts occur relative to electrodes
• Sensitivity kernels: + resistivity anomalies increase app
unless they occur between a current and voltage electrode!

## Slide 4
Field Exercises on Sunday:
• Meet at the loading dock at 10 am
• Dress for a ~ 6–8 hours in the field (layers, sunscreen,
chance of rain!)

## Slide 5
“Sensitivity kernels”
for apparent
resistivity (assumes
a homogeneous
Earth model). This is
a measure of how
much a perturbation
of resistivity at a given
point in the Earth can
be expected to change
the measurement of
apparent resistivity of
the array (reds positive,
blue-greens negative,
yellow ~ zero).

## Slide 6
Resistivity “Pseudosection”:
Measurements are a combination of profiling (different x) &
sounding (different a-spacings)
Plot / contour app versus distance x and a-spacing increment
n, where n = a/a0 and a0 is smallest a-spacing

## Slide 7
(This image from the West Cache fault, collected
in 2012, is an example of an apparent resistivity
pseudo-section):

## Slide 8
Clear from the
earlier modeling
of Wenner array
apparent resistivity
across a vertical
contact that this
approach can
give a VERY
approximate image
with potential for
a lot of “false”
anomalies…

## Slide 9
True inversion of the data will yield a much more accurate
image (for much the same reasons that depth migration
does in the seismic case!)
(Calculated from the inverted model)
Note the change in scaling of the colorbars from pseudo-sections to inverted image!!!

## Slide 10
Resistivity pseudosection from the western trench location
for the East Cache Valley fault zone near Paradise…

## Slide 11
Using resistivity sounding for a two layer model:
Vertical sounding at 25.7 m. Maroon line is measured; blue line
modeled using Excel spreadsheet based on Burger’s Table 5-4.
1 = 101  m, h = 3.22 m
2 = 16.7  m
RMS Misfit 1.897  m

## Slide 12
Can model equally well by using constant thickness and
varying the resistivities, or using constant resistivities &
varying the thickness…
Because these data did not go to a small enough a-spacing
to nail down  in the upper layer.
1 = 101  m, h = 1.72 m
2 = 16.7  m
RMS Misfit 0.847  m

## Slide 13
1 = 100
2 = 17
Layer-over-halfspace modeling suggested a variable-
thickness upper layer with ~ 100 m (Bonneville deposits)
over = 17 (Great Salt Lake fm). The data imply the trenched
geomorphology represents a beach burm deposit instead of
a fault scarp!

## Slide 14
Little Mountain DC Resistivity Profile…

## Slide 15
An inverted model of resistivity structure…

## Slide 16
East Cache
fault in Green
Canyon
Pseudosection and inversion can be very
similar though…

## Slide 18
DC Resistivity: Applications
Lithology application: Sand vs. clay in a study of agricultural
groundwater contaminant plumes.

## Slide 19
Mapping an intrusive dike feature…

## Slide 20
Mapping cave locations in karst terrain.