## Slide 1
Geology 5660/6660
Applied Geophysics
10 Jan 2024
© A.R. Lowry 2008-2024
Read for Fri 12 Jan: Burger 1-21
Last time: Overview of Applied Geophysics
• Important syllabus points: Labs, projects, exams, text, website
• Geophysics:
What is it? Who does it? (Career tracks) And why?
What this class will be about: Geophysical Imaging
Examples:
‹› Seismic reflection imaging of the subsurface under
Upheaval Dome (salt dome, or impact structure?)
‹› Magnetotelluric (electrical) imaging of a mining prospect
Reminder: Be thinking about possible ~nearby field sites!
(We will discuss in the next few weeks!)

## Slide 2
Seismic imaging: A brief thought exercise
!
‘Dja ever count seconds?

## Slide 3
Seismic Concepts I: Velocity
Velocity is the distance traveled per unit time, V = x/t.
Rule of thumb is to count seconds and divide by 3 for
distance in km (or by 5 for distance in miles).
!
Velocity of light in air ~ 3x108 m/s
Velocity of sound in air ~ 340 m/s

## Slide 4
! Different types of materials have different seismic velocities…
Hence in geophysical imaging of the subsurface, we want
to measure changes in physical properties that tell us
something about the structure & materials down there:
Energy
Source
Soil:
Vp = 1 km/s
Limestone:
Vp = 3 km/s
Seismometers or “Receivers”
Sound is a type of wave made up of compressions and rarefactions of atoms. It is also called a “dilatational strain wave”, or in seismology, a P-wave !

## Slide 5
Energy
Source
Soil:
Vp = 1 km/s
Limestone:
Vp = 3 km/s
Seismometers or “Receivers”
Sound waves from an energy source radiate in all directions…
Velocity V = x/t, so in a uniform medium the wave
travels a distance x = VDt in a time t.
Black line is
the “wavefront”,
or location of the
sound energy
furthest from the
source, at time t
Blue arrows are
“rays” in the
direction of wave
propagation
(perpendicular
to the wavefront)
Defn: The surface of furthest travel of a wave at a given time t is
called a wavefront.

## Slide 6
So, a valid (and important) question is, “How does info about
deep layers get back to the surface where we can measure it?”
Seismic Concepts II: Huygen’s Principle
Every point on a
wavefront can be
treated as a point
source for the next
generation of
wavelets. The
wavefront at time t
later is a surface
tangential to the
furthest point on
each of these
wavelets.
Old
wavefront
New
wavefront
Old
wavefront
New
wavefront
cDt
cDt

## Slide 7
Energy
Source
Soil:
Vp = 1 km/s
Limestone:
Vp = 3 km/s
Seismometers or “Receivers”
Thought exercise: Assume the source and seismometers
are all equally spaced at a distance x. Assume the soil
layer is 2x thick. Draw two diagrams showing what you
imagine the wavefront will look like at times 2t1 & 3t1.
x

## Slide 8
Energy
Source
Soil:
Vp = 1 km/s
Limestone:
Vp = 3 km/s
Seismometers or “Receivers”
Black line is the
“wavefront”
at time t = t1
Blue arrows are
“rays” in the
direction of wave
propagation
(perpendicular
to the wavefront)
x
Something important to think about…
Where is the wavefront at time 2.5Dt?
At 2.25t1 and 2.75t1?
Given Huygen’s principle, what does that imply about the
wavefronts?

## Slide 9
Energy
Source
Basalt:
Vp = 3 km/s
Loess:
Vp = 1 km/s
Seismometers or “Receivers”
Now do a similar thought exercise assuming a planar
wavefront in a basalt layer that is 2x thick, over a slower
loess layer. Draw two diagrams showing what you
imagine the wavefront will look like at times 2t1 & 3t1.
x