## Slide 1
Geology 5660/6660
Applied Geophysics
12 Feb 2024
© A.R. Lowry 2008-2024
Read for Wed 14 Feb: Burger 167-199 (§4.2-4.3)
Last time: Seismic Reflection Method:
• A second (or more) layer reflection involves messy
algebra to represent exactly using Snell’s law!
• For a single dipping layer,
• x2 – t2 Method : On a plot of t2 vs x2, for a single layer:
• For dipping layer: Mean slope is ; limb separation


## Slide 2
The x2 – t2 Method plus an assumption of
a single-layer approximation is the
approach taken to inverting data in Reflect!

## Slide 3
This also works for multiple layers–
However instead of explicitly
solving e.g.:
We use an approximation called
the Dix Equation

## Slide 4
h1
V1
x/2
V2
h2
Recall the multiple layer case:
Solving for path length in each layer using Snell’s law
results in a complicated function of all velocities &
thicknesses…
Green’s method: Uses x2 – t2 and ignores bending of
the ray to get approximate thicknesses and velocities of
second, third etc layers using the single-layer equation…

## Slide 5
h1
V1
x/2
V2
h2
Recall multiple layer case:
Green’s method:
Distance
Inverse velocity, weighted by layer thickness
over total thickness

## Slide 6
Dix’ Equation:
Improves slightly on Green’s method because it is a closer
approximation of the true physics. We define a weighted
root mean square (RMS) velocity for n layers
as:
Here ti is the one-way vertical
travel-time through layer i, i.e.,
Then on an x2 – t2 plot, we approximate with the linear equation:
for layer n
;
;

## Slide 7
This means we can
solve for both the
velocity and thickness
in any layer for which
we have a reflection
above & a reflection
below, using observed
parameters of a
line-fit on an x2 – t2
plot!
slope
slope
intercept
intercept

## Slide 8
Caveat:
Recall that Dix’ equation is an approximation.
After refraction in overlying layers, reflections from the 2nd+
interface are no longer truly hyperbolic… e.g. (2-layer case)
contains a (t2 – 2Ct + C 2) term.
Generally, approximation is good for small offsets, poorer
further out.
(We ignored this.)

## Slide 9
Normal Move-Out and the dipping layer problem:
Recall our definition of NMO for a single horizontal layer:
We can write:
The binomial theorem tells us that:
So letting and , and assuming z << 1
(i.e. ) then
and
(An equal-sign with a dot over it denotes truncation of an infinite series!)

## Slide 10
Note: If x is not << 2h, we could expand the series further…
(but that adds computation)
This from the text,
using a 1500 m/s
velocity in a 30 m
thick layer…
Why express the reflection travel-time this way if it is
inaccurate?
Because now we can write TNMO in terms of the observed t0
and (one) unknown velocity!

## Slide 11
NMO correction can be applied to multiple layers using the
Dix equation approximation for Vrms:
But what about dipping layers?
h1
V1


Recall our dipping
layer problem: We can write

## Slide 12
Using the same binomial thm approach we used for a horizontal layer,
can be expanded and truncated as
x2
t2
mean
slope
down-dip
limb
up-dip
limb
Recall the x2 – t2 plot for a
dipping layer: Could average
to get a line with
slope 1/V12, and the difference
between the line and the limbs
related to the dip angle:

## Slide 13
x
TNMO
mean
down-dip
limb
up-dip
limb
We can
similarly use
the (observed)
difference
between
up-dip &
down-dip NMO
to estimate dip
via:
Binomial series approximation: