## Slide 1
Geology 5660/6660
Applied Geophysics
14 Feb 2024
© A.R. Lowry 2008-2024
Read for Fri 16 Feb: Burger 167-199 (§4.2-4.3)
Last Time: Seismic Reflection Methods
• Dix Equations for multiple layers:
approximates the true physics by neglecting a
t-to-the-first-power dependence in Snell’s law…
• But Dix’ equations enable us to use (observed) slopes and
intercepts in a t2 vs x2 plot to estimate velocities and
thicknesses of layers bounded by reflections
• Normal move-out can also be approximated from
(observed) t0 and an estimated velocity as (e.g., 1st order):

## Slide 2
Last Time Continued:
• Dipping Layer Problem:
 Using t2 on x2–t2 plot: (works for 1-layer!)
 Using TDMO approximation on a TNMO vs x plot:
(works for n-layers!)

## Slide 3
Some practical considerations (a reminder!):
For x2 – t2 methods & Dix Equations:
Dix equation approximation of Vrms is most valid for
small-offset (near-vertical) rays; validity of approximations
decreases with distance
For reflection seismic in general:
NMO approximations in terms of t0 require x << 2h1 (i.e.,
small-offset, near-vertical rays)
Reflections from shallow interfaces will be overwhelmed
by other arrivals at small-offsets

## Slide 4
Burger refers to an “optimal window” at distances beyond
interference from low-V waves, but also must get beyond
direct & refracted wave interference to observe confidently
“Optimal
window”
(Industry seismic)

## Slide 5
Practical considerations cont’d:
Multiples are waves that travel the two-way travel path
between two interfaces more than once:
Recognizable as having:
About twice the travel-time of the primary
The same apparent velocity but twice the thickness
from x2 – t2 analysis
Less move-out and lower amplitude than the primary
Primary
Primary
Multiple
Multiple

## Slide 6
Practical considerations cont’d:
Multiples are waves that travel the two-way travel path
between two interfaces more than once:
The furthest reflection image point for a primary reflection
is ~half the distance to the furthest geophone…
But the furthest image point for a first multiple extends to
¾ the distance (and higher multiples further!). Thus,
multiples (if used!) can extend the profile imaging aperture
Primary
Multiple
Multiple

## Slide 7
V1
V2
Diffractions: Recall diffractions in the refraction method:
Observationally, impossible to distinguish diffracted arrival
associated with a step from a smooth thickness change over
one wavelength (10–20 m for 100 Hz)

## Slide 8
V1
Diffractions:
h1
h2
x
The diffraction travel time is time ts = rs/V1 from the source
to the step edge plus time td from step to geophone at a
distance xg from the step
rs
xg

## Slide 9
Worth noting: In migration of seismic data, we “migrate” travel-times
to what they would be for a zero-offset source by correcting for NMO,
but diffractions have a different moveout! After correcting for NMO,
(layer with no offset)
(layer with offset)
diffraction
twtt
(Smile!)

## Slide 10
In typical seismic images we plot two-way travel-time
increasing downward (to simulate depth) so “smiles” are
flipped upside-down to form “frowns”
So (prior to diffraction migration processing!) these can
be a diagnostic tool to help recognize faults, salt diapirs
and other sharp lateral changes in velocity…

## Slide 11
Some practical considerations continued:
Emphasize high frequencies to better differentiate from low-f
arrivals (e.g., surface waves) & improve resolution
Vertical resolution: Recall V = f
(high frequency = short wavelength)
Theoretical limit of resolution for a thin bed is h = /4
(& in the practical limit h will be > /2)
h = 7.5 m
 = 10 m
 = 20 m

## Slide 12
Standard Migration
High-end Migration
Courtesy of ExxonMobill
Well-Parameterized (Velocity)
Migration Enhances Resolution
These two images differ because of processing parameters, not source frequency… But note the difference in clarity for interpretation if the impedance contrast wavelets are “sharpened”
by emphasizing higher frequencies!

## Slide 13
Frequency also determines horizontal resolution:
The first Fresnel zone (approximate area of the reflector
responsible for a signal) has radius
R
“Fresnel zone”
For V = 1500 m/s, f = 150 Hz, h = 20 m  R = 10 m

## Slide 14
To emphasize high frequencies we use:
Geophones with high natural frequency ~ 100 Hz
Filters to remove low-frequency arrivals
High-rate sampling to avoid aliasing
High frequency source (e.g., dynamite, vibraseis)
To image with high resolution, must also avoid
spatial aliasing (i.e., geophone sampling must be
relatively close!)
2000 Hz  2000 samples per second