## Slide 1
Geology 5660/6660
Applied Geophysics
Last Time: Magnetotelluric (MT)
• Magnetotelluric (MT) measures 3D magnetic field H, horizontal
electrical field E in time series to get electrical resistivity structure:
where sd is averaged resistivity over an
-dependent skin depth.
• Passive method  sources include lightning strikes (10,000–1 Hz;
ionospheric resonances (1–.001 Hz); ionospheric disturbances
(.001–very low Hz)
• Some (minor but growing) applications in oil & mining; commonly used
in large scale studies of tectonics, melts and volatile/fluid transport
• EarthScope data show evidence of (primarily E-W trending) small-scale
melt bodies under W-C Snake River Plain and widespread melt in
lower crust of the Basin-Range province!
• Likely to grow in usage in the future
17 Apr 2026
© A.R. Lowry 2008-2026

## Slide 2
Wireline Logging
describes a suite of geophysical tools that are lowered
into a well (often oil & gas; sometimes water, mining, or
environmental monitoring) to record physical properties of
the down-hole environment.
Much cheaper than coring (~$15–60 per m, plus transport);
provides in situ information on medium that can’t be gained
from core & enables “ground-truthing” of physical properties
imaged by surface geophysics.
Main types include:
• Electrical (resistivity, spontaneous potential)
• Nuclear (active and passive gamma, neutron)
• Seismic (sonic  acoustic (i.e. P-wave), velocity log)
• “Other ” (caliper, temperature, camera, magnetic
susceptibility, …)

## Slide 3
Applications matrix (from the
IODP-USIO website at Lamont-
Doherty)

## Slide 4
Typically a single wireline
tool will include several
different sources and
sensors to maximize
efficiency…

## Slide 5
Borehole television or televiewer (acoustic reflection) is useful
to get fracture orientations, breakouts & drilling-induced tension
fractures ( stress orientation; caliper also gives this). When
compared to unrolled images of core, image correlation enables
correction to true depth & true orientation of the core.

## Slide 6
Electrical Logging
is perhaps most similar to stuff we’ve already seen.
Resistivity logging uses four or more electrodes (two+
current, two+ voltage) to measure apparent resistivity of the
well environment. Often use different spacings to image
“shallow” and “deep”; may also measure  of borehole fluid.
Recall resistivity dependence:
Low a
High a
shale, clay
sandstone, limestone
brine
freshwater, hydrocarbon
high
low
Lithology
Pore Fluid
Porosity
So resistivity is used in combination with other
logs to infer lithology, porosity, pore fluids. FMS
(formation microscanner; here “focused”) also yields
dip, structure, foliation & correlation to core...

## Slide 7
fresh water or hydrocarbon
in porous limestone/sandstone;
Spontaneous Potential Logging we’ve
already seen… Low SP indicates interaction
of brine fluids with drilling mud disturbance.
Low SP
High SP
Low a
High a
brine in porous
limestone, sandstone
shale
tight limestone
or sandstone
So SP is used in
combination with other
logs (especially resistivity)
to infer lithology, pore fluid
type, permeability

## Slide 8
Induced Potential also gets used in a borehole context, but
as in the case of surface surveys, it is used primarily for
mining and environmental monitoring applications.
Here, cross-
borehole
imaging shows
high resistivity
associated with
a metasomatic
granite; high
chargeability
indicates sulfides
accompanying
trace deposits
of gold.
Resistivity
Chargeability

## Slide 9
Nuclear Borehole Logging
uses either passive or active recording of radioactive
(nuclear fission) emissions.
Natural Radioactivity
logging records spectral
content of passively-sensed
gamma rays produced by
fission. Spectra are different
for different radioactive
elements so measure
concentrations of K, U, Th in
the formation.
Radioactivity in sediments
generally means weathered
by-products of feldspar, so
mostly used to infer lithology (although it also has
implications for cementation, permeability, strat correlation).
(courtesy Kansas
Geological Survey)

## Slide 10
Generally
speaking,
low gamma
means clean
sandstone or
limestone;
high gamma
indicates
presence of
shale.
Proc Oc Drill Prog v198, 2001
(courtesy Kansas Geological Survey)

## Slide 11
Profile of Permian to Upper Cretaceous -logs for a basin
in western Kansas

## Slide 12
Aside:
Aero-spectral
gamma also has
applications in mining
industry and other
exploration problems
K
U
Th
Duval et al., USGS Open File Rep 2005-1413

## Slide 13
Total “” natural radioactivity of various rocks
Nuclear Logging:
Anhydrite and Gypsum
Gabbro and Basalt
Coal
Limestone and Dolomite
Sandstone - Orthoquartzite
Caliche
Shale
Schist and Gneiss
Granite and Rhyolite
Potash and Phosphate Beds
Increasing Total Gamma
Some Lignites
Arkose
Red
Bentonite
Organic