## Slide 1
Geology 5660/6660
Applied Geophysics
22 Jan 2024
© A.R. Lowry 2008-2024
Read for Wed 24 Jan: Burger 27-60 (Ch 2.2.2–2.6)
Last time: Quick derivation of the Seismic Wave
Equation:
Stress, strain and displacement waves:
 Rheology is linear elastic:  = c (Hooke’s Law)
 We use Lamé’s elastic constants (l, m)
• The elastic wave equation:
 Assumes an isotropic solid
 Stress/strain relations assume infinitesimal strain
so that strain is the derivative of displacement:  = ∂u/∂x
 Results in the seismic wave equation(s) and
seismic velocities:

## Slide 2
Last time continued: Seismic velocity:
• Velocities are more sensitive to  &  than to ; depend on
porosity, lithology, cementation, pressure, temperature, fluids!

## Slide 3
isometric view
cross-sectional view
Geophone:
Commonly-used by industry, less
often for academic, seismic
reflection studies
Often vertical component only
Often low dynamic range
Undamped response
of mechanical system
Response after
electronic damping
10 Hz “natural frequency”
10
100
20
500
200
A Seismometer differs in cost &
componentry… 3-c, > dynamic range

## Slide 4
“Recall” that an idealized mass on a spring is a
harmonic oscillator : Position x of the
mass follows the form x = A cos (t + )
where A is amplitude, t is time,  is the natural
frequency of the spring, and  is a phase
constant (tells us where the mass was at
reference time t = 0).
x
A
T = 2/
In the frequency domain this
is a spike or delta-function:

Understanding the Frequency Domain:

## Slide 5
Signal recorded by a seismometer is a convolution of the
wave source, the Earth response, and the seismometer
response.
Wave
Source
Earth
Response
Seismometer
Response
where  denotes convolution:
Example:
=
So, we want seismometer response
to look as much as possible like a
single delta-function in time:
t = 0





Two “useful facts” to know about the frequency domain:
(1) A convolution in the time domain is a simple multiplication in frequency domain
(2) A delta-function (or “spike”) in one domain is a sinusoid in the other. A spike at zero is a constant!

## Slide 6
Seismometer response is given by:
where i is current, 0 is “natural frequency” of the
spring-mass system oscillation, K is electromagnetic
resistance to movement of the coil, R is electrical
resistance to current flow in the coil, & x is movement
of the mass relative to the coil.
The damping factor h is given by:
where  is the mechanical
damping coefficient.
Hence we choose K and R to give a time response that
looks as much as possible like a delta-function (= a flat
frequency response):

## Slide 7
This corresponds to 0/h = 1: Critical damping
Critically Damped
Overdamped
Underdamped
Seismometers typically are designed to be slightly
overdamped (0/h = 0.7).

## Slide 8
Seismometer Damping
Source Function
An explosion at a depth of 1 km & t = 0
is recorded by a seismometer at the
surface with the damping response
shown. What will the seismogram look
like?
V = 5 km/s

## Slide 9
The Key Takeaway:
 A Seismogram (or geophone recording) is not an
exact record of ground displacement
 Instead, it approximates motion (usually acceleration)
delayed by some amount
 By knowing the seismometer response (and
“deconvolving” by dividing it out in the frequency
domain), we can correct to approximate true ground
motion in a limited frequency band

## Slide 10
(Note: for really big signals, can get more robust operation
and lower frequencies from other types of instruments…
E.g. GPS!)
4 April 2010 M7.2 Baja California earthquake