## Slide 1
Geology 5660/6660
Applied Geophysics
24 Apr 2024
© A.R. Lowry 2008-2024
Review for Final Exam
(Comprehensive)

## Slide 2
8 Jan: Overview of Applied Geophysics
• Important syllabus points: Labs, projects, exams, text, website
• Geophysics:
What is it? Who does it? (Career tracks) And why?
What this class will be about: Geophysical Imaging
Examples:
‹› Seismic reflection imaging of the subsurface under
Upheaval Dome (salt dome, or impact structure?)
‹› Magnetotelluric (electrical) imaging of a mining prospect
Reminder: Be thinking about possible ~nearby field sites!
(We will discuss in the next few weeks!)

## Slide 3
10 Jan: Seismic Waves: A thought exercise
• The fundamental observable of seismic imaging is the
wave propagation velocity : V = Dx/Dt
• Different types of materials have different seismic velocities
that depend on both density & elastic properties …
(but predominantly the latter!)
A Wavefront is the surface of furthest wave disturbance
at a specific time t. A ray is the wave propagation direction
& is always normal to the wavefront!
Huygen’s principle: Every point on a wavefront can be
treated as a point source for the next generation of
wavelets

## Slide 4
12 Jan: Course Overview
• Fundamental elements of every geophysical imaging tool:
Instrumentation (how it works; sensitivity; and what
specific types of observations it collects)
Sampling in both space and time
Theory (equations, assumptions, approximations, and
whether/how the data are skeletalized)
Noise (what is the noise source, how do we remove it,
and when is the noise… Not?)
Interpretation (what is ambiguous in the data?
What features of an image could lead to
misinterpretation?)

## Slide 5
17 Jan: Brief Intro to Seismology &
stress & strain in an elastic medium:
Four types of seismic waves:
 P (“Primary” = sound; a body wave)
 S (“Secondary” = shear; also a body wave)
 Surface waves (Love & Rayleigh: at free surface only)
 Normal Modes (“Resonant tones” = standing waves)
An abbreviated introduction to stress and strain:
 Stress s, strain e and displacement waves propagate
in a medium
 Rheology is linear elastic:  = c (Hooke’s Law)
 Defined several elastic constants (E, , K) & Lame’s
parameters m & l

## Slide 6
19 Jan: Quick derivation of the Seismic Wave
Equation:
Stress, strain and displacement waves:
 Rheology is linear elastic:  = c (Hooke’s Law)
 We use Lamé’s elastic constants (l, m)
• The elastic wave equation:
 Assumes an isotropic solid
 Stress/strain relations assume infinitesimal strain
so that strain is the derivative of displacement:  = ∂u/∂x
 Results in the seismic wave equation(s) and
seismic velocities:
• Velocities are more sensitive to  &  than to ; depend on
porosity, lithology, cementation, pressure, temperature, fluids!

## Slide 7
22 Jan: Instrumentation:
• A seismometer (or geophone) is an inertial mass
that moves relative to a frame, coupled to the ground
• Mass = magnet (or coil) moves wrt coil (or magnet);
Voltages are amplified and recorded as signal.
• Motions are damped to maximize signal & minimize “ringing”
Useful Concepts: Time & Frequency Domains
• Time (t)-dependent signals (time domain) can be expressed
as amplitudes of sums of sin(t) & cos(t) for all frequencies 
(frequency domain).
• A Seismogram is t-domain convolution (-domain
multiplication) of source, Earth response, instr. response

## Slide 8
24 Jan: Fermat’s Principal & Snell’s Law:
• Fermat’s principle (the propagation path or raypath is
always the path requiring least time) leads to Snell’s
Law :
Snell’s law predicts (for example) that a ray entering a slower
medium bends away from the boundary
• Reflections & Refractions: A wave traveling across a
boundary conserves energy ; has continuous stress
& displacement  reflects some energy, transmits some
energy, and often converts some energy to another
phase (e.g. P to S).
• All are governed by Snell’s Law!
Here, q is the angle of incidence between the raypath and the normal to a boundary separating two media (1, 2) with different velocities V1 and V2

## Slide 9
24 Jan continued:
• The Critical Angle is the angle of incidence for which the
refraction parallels the interface:
(& at > angles, no refraction!)
• Diffractions occur at “scatterers” or non-ideal
boundaries; are predicted by Huygen’s Principle but not by
ray theory/Snell’s Law.

## Slide 10
26 Jan: Fundamentals of Seismic Amplitudes
• The Impedance of a medium is Z = V. Reflected and
refracted amplitudes depend on the impedance contrast
via reflection & refraction coefficients (for normal-incidence):
• Source amplitude determines the total energy in an
(idealized) elastic wave
• Geometrical Spreading distributes energy over
increasing surface area of the wavefront.
Uniform half-space spherical spreading:

## Slide 11
26 Jan continued: Amplitude
• For a refracted head wave, geometrical spreading is
cylindrical spreading :
• Anelastic Attenuation converts part of the elastic
wave energy to work and depends on Quality Factor Q:

## Slide 12
29 Jan: Seismic Amplitudes
• Attenuation quality factor Q is another physical rock property
that gives different information than velocity (more sensitive
to shallow porosity & fluids, deep temperature, melt & volatiles)
• Q is hard to measure though because amplitudes also depend
on energy partitioning (i.e., mode conversions),
multipathing, and scattering
• Still, Q can help to interpret seismic images (if you can measure
it)!

## Slide 13
29 Jan continued: Zoeppritz Equations
• Mode Conversion (P to S or S to P) occurs when  ≠ 0
• Introduced the ray parameter (based on Snell’s Law):
 Predicts propagation paths if ,  structure is known!
• Continuous displacements ( , ) and stresses
( , ) provide four equations in five unknown
amplitudes of incoming and outgoing waves… Normalize
by amplitude of incoming wave gives Zoeppritz’ equations
• Graphical user interface models of Zoeppritz’ equations are at
http://www.crewes.org/ResearchLinks/ExplorerPrograms/ZE/

## Slide 14
31 Jan: Zoeppritz’ equations and AVO
• Zoeppritz’ equations give amplitudes of reflections and
refractions that vary with angle of incidence at a boundary
• Amplitude vs offset (AVO) uses reflection amplitudes
at different offsets (hence different i0) to infer properties
The Refraction Method:
• For a single horizontal layer over a halfspace,
observed travel-times for direct and refracted arrivals:
give the velocities and layer thickness from t = mi x + bi as:

## Slide 15
2 Feb: The Refraction Method:
• For a single horizontal layer over a halfspace,
observed travel-times for direct and refracted arrivals:
give the velocities and layer thickness from t = mi x + bi as:
• The crossover distance xco can be used
in experiment design, to ensure adequate
geophone sampling:

## Slide 16
2 Feb continued: The Refraction Method:
• For an n-layer Earth:
• Single Dipping Layer Boundary:
 Requires reversed profile to separate dip from velocity
 Travel-times going “up-dip” (ud) and “down-dip” (dd) are:
 Can calculate velocities, dip angle , & thickness:

## Slide 17
5 Feb: Refraction With Dipping Layers
• Algebraic solution for parameters (thickness, dip, velocity)
of subsurface structure from observations (travel times)
is a simple example of data inversion
• Refract solves for multiple dipping layers using the
Adachi formulation…
• Limitations of the Refraction Method:
 Do not get returns from low velocity layers
 Can alias or miss entirely thin layers
Deeper layer thicknesses are overestimated for the
first case; underestimated for the second

## Slide 18
5 Feb Continued: Refraction in Non-Ideal Media:
• Velocity changes within layers can be distinguished by
similar slopes (forward & reversed) over same locales
• Change in thickness  change in intercept time
• Single step change in thickness h:
 In t-x plot, similar slopes before & after a shift in intercept
(with opposite sign forward vs reversed)
Here, t0 is intercept of a line fit (earlier we used b for intercept!)

## Slide 19
7 Feb: Refraction in Non-Ideal Media:
• Plus-Minus Method for arbitrarily changing h:
 where m– is slope of a plot of t1i–t2i vs xi for SP1, 2 and
geophones i
The Reflection Seismic Method:
• Seismic Reflection Travel-Times have eqns of a
hyperbola. For a single layer,
has intercept 2h1/V1 and
slope of the asymptote is 1/V1!
• Defined Normal Move-Out (NMO) as the reflection
travel-time at distance x minus the intercept (t at x = 0):
(NMO is used to shift reflection arrival times and make two-way travel time images!

## Slide 20
9 Feb: Seismic Reflection Method:
• A second (or more) layer reflection involves messy
algebra to represent exactly using Snell’s law!
• For a single dipping layer,
• x2 – t2 Method : On a plot of t2 vs x2, for a single layer:
• For dipping layer: Mean slope is ; limb separation


## Slide 21
12 Feb: Seismic Reflection Methods
• Dix Equations for multiple layers:
approximates the true physics by neglecting a
t-to-the-first-power dependence in Snell’s law…
• But Dix’ equations enable us to use (observed) slopes and
intercepts in a t2 vs x2 plot to estimate velocities and
thicknesses of layers bounded by reflections
• Normal move-out can also be approximated from
(observed) t0 and an estimated velocity as (e.g., 1st order):

## Slide 22
12 Feb Continued:
• Dipping Layer Problem:
 Using t2 on x2–t2 plot: (works for 1-layer!)
 Using TDMO approximation on a TNMO vs x plot:
(works for n-layers!)

## Slide 23
14 Feb: Seismic Reflection Methods
• Practicalities : Approximations valid for small offsets only; reflections
visible in optimal window; note multiples! (which still can be used
to add information to imaging!)
• Diffractions: For a truncated layer boundary, travel-time
of the diffraction has different moveout than reflection energy
 After migration, diffraction will remain as a “smile ”
(and in seismic section, shows up as a “frown ”)
• Resolution is frequency-dependent:
 Vertical resolution is theoretically h  /4 (but practical limit h > /2)
 Horizontal resolution limit is pixel with radius:

## Slide 24
14 Feb: Seismic Reflection Methods (continued)
• Hence we strive to get high frequencies:
 Geophones with natural frequency 100 Hz; filter out low-f
 High sample rate to avoid aliasing
 High frequency source
• Because of attenuation, resolution is generally better
for shallow imaging; gets poorer with increasing depth

## Slide 25
16 Feb: Seismic Reflection Data Processing
• Processing Step I : Static Correction for elevation,
weathered (or soil) layer velocity & thickness:
OR shift all traces to enforce a head wave slope 1/V1
• Step II : Dynamic Correction for Normal Move-out
using velocity analysis to optimize stacking velocities
VS(t0) at every possible t0 for each source
 automate by maximizing stack amplitude or
cross-correlation

## Slide 26
16 Feb continued: Reflection Data Processing
• Step III : Stacking (Common Midpoint Gathers)
Sum all NMO-corrected traces that have a common midpoint
for the source-receiver pair, and position that trace at
the midpoint location on the image…
However, dipping layers will be out of place.
Results e.g. in “bow-ties”
• Step IV: Time Migration rotates reflection energy to its
“true” location on a two-way travel-time image. Use multiple
source-receiver midpoints to determine where in 2wtt energy
must derive to get a continuous surface! For a dipping layer
and neighboring traces with different
intercepts t0a and t0b separated by x:

## Slide 27
21 Feb: Reflection Data Processing Cont’d
• Step V : Time Migration returns reflection energy to its
“true” location on the two-way travel-time image… Depth
migration uses velocity structure (from NMO analysis)
to convert travel time to depth (improving image resolution)
• Step VI : Reform amplitude stacks of source-receiver pairs
using Common Depth Point (CDP) instead of Common
Mid Point (CMP) and repeat Step V
• Sometimes additional steps as well:
 Amplitude adjustments
 Frequency adjustments
 Transmission adjustments

## Slide 28
21 Feb: Reflection Seismic Interpretation
• Data collection: Huge quantities of data! Redundancy is key!
• 2D profiling still used for initial reconnaissance, but 3D is
industry standard for prospects
• Deep crustal imaging is only done in 2D; shows “reflectivity” in
crystalline basement from low angle faults & foliated minerals

## Slide 29
23 Feb: Reflection Seismic Interpretation
• 3D gives higher resolution, better positioning (because it
enables migration of “out-of-plane” seismic reflection energy)
• Vertical resolution : Whether or not a layer is “visible”
to seismic reflection depends in part on properties of the layer
(including both thickness and impedance contrast)
• Lateral resolution : Faults are not directly imaged but
inferred from both layer offsets and “blurring” caused by
near-fault scattering of seismic energy

## Slide 30
26 Feb: Seismic Reflection Interpretation
• Seismic quality depends on:
 Acoustic impedance contrast
 Depth ( frequency)
 Layer thickness ( interference)
 Properties of overlying layers
 Source energy
 Processing parameters
 Acquisition direction
 Instrumentation
• Seismic inversion seeks Physical Properties
• Trace cross-correlation is used to map fault offsets
• Depth migration required for accurate depths and
geometries of structures

## Slide 31
26-28 Feb: Industry Seismic Interpretation
• Seismic inversion = using velocity information for physical
properties, true depth, better resolution via depth migration
• 3D visualization (“data caves”) an important part of interpretation
• 4D seismic: Multiple 3D reflection images over time aid in
optimization of reservoir models and production
• Salt structures are especially challenging but have been a
focus of innovation
• EM imaging is a tool of growing importance; electrical
resistivity is sensitive to fluids and clay content
• Knowledge of geological processes is key to
interpretation!!!! BUT, it’s critically important to
also understand attributes/artefacts/limitations
of the seismic reflection data.

## Slide 32
1 Mar: Ground Penetrating Radar (GPR)
• Radar = electromagnetic radiation (light) in the
50-1000 MHz (radio) frequency band
 Governed by wave equation ( similar to seismic!)
 Source & receiver are dipole antennae
 Signal is a single pulse
 Processing & display analogous to seismic section
 High frequency  high resolution (but also...)
 High attenuation
 Images variations in electromagnetic impedance Z

## Slide 33
1 Mar: Ground Penetrating Radar
• Radar reflections image variations in Dielectric permittivity
(real part  = permittivity)
 3-40 for most Earth materials;
 higher when H2O &/or clay present
• Radar attenuation similar to seismic: where:
 higher for clay, silt, brines; limits imaging to upper few m
• Velocity is not estimated (rather depth is approx. from ~V)
 (but can be estimated from
NMO or diffraction moveout!!!)

## Slide 34
4 Mar: Ground Penetrating Radar
• Radar reflections image variations in Dielectric permittivity
(real part  = permittivity)
 3-40 for most Earth materials;
 higher when H2O &/or clay present
• Radar attenuation similar to seismic: where:
 higher for clay, silt, brines; limits imaging to upper few m
• Velocity is not estimated (rather depth is approx. from ~V)
 (but can be estimated from
NMO or diffraction moveout!!!)
• Standard “processing” includes static corrections for
elevation, filtering, AGC

## Slide 35
8 Mar: Introduction to Gravity
• Governed by LaPlace’s equation:
with solution of the form:
• If we have a spherical body with mass M and constant (or
radially symmetric) density, this integral becomes:
• Method looks for anomalies in gravity g (relative to
the gravity expected for a uniform-density ellipsoid)
that result from lateral changes in mass density 

## Slide 36
18 Mar: Gravity Measurements
• Measurements may be surface-based (i.e., taken with
instruments placed on the ground surface) or
space-based; absolute or relative
• Surface measurements are accurate to ~3-6 Gals (for absolute
gravimeters or relative measurements by Lacoste-Romberg):
i.e., nearly one part in 109 of the total acceleration!
• Satellite measurements (especially GRACE, GOCE) can be
extremely accurate (<0.1 Gal!), but only as an average
over very large spatial scales (> 500 km)
• Time-variable gravity can be useful for understanding
dynamical processes (fluid envelopes & solid Earth)
• Surface-based time-variable g also used for environmental/
hydrologic applications

## Slide 37
20 Mar: Gravity Reduction
• For terrestrial measurements, we record measurement time
and atmospheric pressure; correct for lunar, solar,
planetary & solid Earth tides + atmospheric mass
• Measurement latitude  correction for ellipsoidal height and
centrifugal force of Earth’s rotation (see text eqn 6.12)
• Free air correction is ~ –308.6 Gal/m:
• Free air anomaly :
• Bouguer slab correction :
• Complete Bouguer anomaly :
(Dcorr is instrumental drift;  = 2670; Tcorr is terrain correction)

## Slide 38
22 Mar: Density; Gravity Anomalies & Modeling
• Model structures as having anomalous mass density D
 lithology, porosity, temperature (lowest for soils/seds,
higher for lithified sed rocks, highest for crystalline rocks)
• Gravity anomaly due to a sphere:
(represents only the “vertical” component
of the total vector anomaly!)
where: R is radius of the sphere; d is
depth of the sphere’s center; Dr is the difference in density
from surrounding; and x is horizontal distance from the
center of the sphere.

## Slide 39
25 Mar: Gravity Anomalies & Modeling
• Discussed nonuniqueness:
 Different density (but same mass, same center of mass)
can yield an identical gravity anomaly!
 Different shape at a shallower depth can yield the exact
same gravity anomaly!
(But all geophysical/geological models are nonunique…
Gravity provides info others can’t!)
• Anomalies for:
horizontal cylinder:
vertical cylinder:
fault-bounded block:

## Slide 40
27 Mar: Introduction to Magnetic Methods
• Governed by Poisson’s eqn:  2u = f (sources)
• Source is a dipole rather than monopole
• Magnetic field strength relates to force exerted by
the dipole on a
hypothetical unit monopole:
• Intensity of induced magnetization by an external field is
(where k = m – 1 is magnetic susceptibility)
• Crustal minerals can be diamagnetic (k ~ –10–5);
paramagnetic (k ~ 0.02–0.2); antiferromagnetic
(k ~ 0.05); or ferrimagnetic (k ~ 0.5–10)
• Core minerals (native metals) are ferromagnetic…

## Slide 41
29 Mar: Magnetic Methods
• A magnetic anomaly is the (vector) perturbation of
the external (core) magnetic field’s vector magnitude (HE)
by crustal magnetization
• Magnetic field strength decays as 1/r3
• Total intensity of magnetization:
where remanent magnetization IR is in the direction
of HE at the time of magnetization… i.e., when the rocks
cooled through their Curie temperature
• Must know strength & direction of the Earth’s
main field to model source geometries and
susceptibility contrasts!

## Slide 42
1 Apr: Earth’s Main Magnetic Field
• Earth’s Main Field derives from its “core dynamo”…
convective flow of Ni-Fe outer core + coriolis forces ( +
feedback)  electrical current flow  magnetic field
( + feedback) + crystalline Fe inner core
( + feedback)
• Mostly dipolar, oriented ~ (and precesses around) Earth’s
rotation axis; varies nonlinearly over time…
• Express the vector field at a point as either intensity HE,
inclination i, declination d or local Hx, Hy, Hz (N,E,U)
cartesian components:

## Slide 43
1 Apr: Magnetic Measurements
• Distinguish Main Field from crustal sources by scale: spatial
wavelengths > 2500 km (spherical harmonic degree n < 16)
dominated by core dynamo; smaller scales are mostly crustal.
• Instrumentation:
 Fluxgate magnetometer: Measures field intensity
in the direction of orientation of the coils
 Proton precession magnetometer: Measures
intensity of the total field

## Slide 44
3 Apr: Magnetics (Measurement, Modeling)
• Data collection: remove/avoid metal; be wary of solar activity.
• Reduction: subtract variations in main field (significant on
scales > a few hundred meters in latitude & height)
• World Magnetic Model calculator at:
https://www.ngdc.noaa.gov/geomag/calculators/magcalc.shtml#igrfwmm
• Induced magnetic field due to a dipole is given by:

## Slide 45
5 Apr: Magnetic Modeling
• Induced magnetic field due to a dipole is given by:
• Magnetic field for an arbitrarily-shaped body is:
• Often we use analytical solutions derived for simple
body shapes, e.g., for a sphere of radius R:
• Semi-infinite sheet:
• GravMag uses Talwani solutions for 2D prisms…

## Slide 46
5 Apr: Intro to DC Electrical Resistivity
• DC Resistivity : inject electrical current across two (source
& sink) electrodes, measure voltage across two others.
• Governing equation derives from Maxwell’s equations
to get Ohm’s Law:
• Material property imaged is rock resistivity :
 Low for clays, shales, graphite; intermediate for soils/
unconsolidated seds; high for consolidated seds and
crystalline rocks
 Sensitive to sulfides, temperature, pore fluids

## Slide 47
8 Apr: Electrical Resistivity
• DC Resistivity: inject electrical current across two (source
& sink) electrodes, measure voltage difference DV across two
others.
• Given known distances r between current electrodes (+ = 1, – = 2)
and voltage measurement electrodes (+ = a, – = b) and a known
injection current I, the apparent resistivity rapp:
is an expression of the measurement that assumes the
medium has constant resistivity r (but in reality it is a “weighted
average” of the subsurface resistivity).

## Slide 48
10 Apr: DC Electrical Resistivity
• Electrode Arrays:
 Wenner (constant spacing):
 Wenner-Lee (local voltage measurements)
 Schlumberger (move only current
electrodes):
 Dipole-dipole
 Pole-dipole (simple approach for tunnels/karst)
• In a layered medium, current penetration into a
second layer depends on depth of layer interface,
resistivities as:
where

## Slide 49
10 Apr: DC Electrical Resistivity
• One-Dimensional Sounding:
 Layer-over-halfspace: Wenner app ~  for a/z small;
~ 2 for a/z large
 Two layers over halfspace: May or may not pick up
sandwiched layer depending on thickness, contrast
 Resist does multiple layers, 1D, log a-spacing steps
• Profiling: Vertical contact: app depends on where resistivity
contrasts occur relative to electrodes
• Sensitivity kernels: + resistivity anomalies increase app
unless they occur between a current and voltage electrode!

## Slide 50
12 Apr: DC Resistivity Modeling/Inversion/Interp
• Sensitivity kernels: + resistivity anomalies increase app
unless they occur between a current and voltage electrode!
• Apparent Resistivity Pseudosection is a “weighted
average” of resistivity structure (but with artefacts!)…
• Inversion of resistivity data (i.e., optimal parameterization of
a forward model) uses the physics of the voltage response to
give more structural detail and confidence.
• Applications including permeability mapping, lithologic
mapping, karst & tunnel detection
• Successfully used to inform past field studies for this class!

## Slide 51
15 Apr: IP (Induced Polarization)
• Induced Polarization (IP) measures the chargeability
of transient voltage after DC current is shut off
(time-domain IP) or the phase of voltage relative to a
sinusoidal AC current (frequency-domain IP)
• Results from overvoltage (charge buildup)
 ~ boundaries between ionic & electronic conduction
 by electrodialysis (membrane effect) in clays
• Chargeability ~ anticorrelates with resistivity; highest for
sulfide ores
• IP in the frequency domain can afford more information!
• Heavily used in mining industry; sometimes in well logging
and environmental applications

## Slide 52
15 Apr: Self-Potential (SP)
• Spontaneous Potential (SP): “Natural” amperage (i.e.,
without our injecting current) can arise from:
 Brine infiltration of drilling mudcake in permeable
formations (petroleum industry wireline application)
 Oxidation/reduction reactions at the water table (mining)
 Streaming potential in cavities (karst investigations)

## Slide 53
17 Apr: Magnetotelluric (MT)
• Magnetotelluric (MT) measures 3D magnetic field H, horizontal
electrical field E in time series to get electrical resistivity structure:
where sd is averaged resistivity over an
-dependent skin depth.
• Passive method  sources include lightning strikes (10,000–1 Hz;
ionospheric resonances (1–.001 Hz); ionospheric disturbances
(.001–very low Hz)
• Some (minor but growing) applications in oil & mining; commonly used
in large scale studies of tectonics, melts and volatile/fluid transport
• EarthScope data show evidence of (primarily E-W trending) small-scale
melt bodies under W-C Snake River Plain and widespread melt in
lower crust of the Basin-Range province!
• Likely to grow in usage in the future

## Slide 54
19 Apr: Borehole logging
• Wireline Logging is the practice of lowering a geophysical
tool down a well to measure physical properties in situ
• Single logs are (often) ambiguous; combine logs to get
lithology, porosity, pore fluid type
• Important for:
 Relating core to the in-situ borehole environment
 Relating surface seismic to the in-situ borehole environment
 Determining formation lithologies, porosity, fluid chemistry
 Temperature for thermal/hydrocarbon maturation studies
 Guiding drilling operations
• Borehole televiewer (from P reflections) gives fracture properties,
“dipmeter”, log/core correlation

## Slide 55
19 Apr: Wireline Logging
• Resistivity logs work on similar principles to surface DC
resistivity method; low  implies shale, clay or briny fluid
• Low Spontaneous Potential (SP) indicates presence of
high-porosity/permeability, brine-filled formations
• Natural Radioactivity (“Gamma”) Log measures high
energy EM ( -freq) radiation; multi-spectral  concentrations
of K, Th, U elements. Useful for shale content, cementation,
some detrital minerals, strat correlation, paleosols...

## Slide 56
22 Apr: Wireline Logging
• Formation density (g–g) logs send gamma radiation into
the formation and record backscatter from electrons to
approximate density
• Neutron log emits neutrons; records emitted gamma to
estimate density of hydrogen (related to porosity)
• Sonic Log measures travel-times for seismic sound waves;
can be combined with e.g. neutron log in a crossplot to
calculate lithology and porosity
• Vertical seismic profiling (VSP) lowers geophones into
the borehole; uses surface sources to relate borehole seismic
to surface seismic imaging at similar sampling/frequencies