## Slide 1
Geology 5660/6660
Applied Geophysics
26 Jan 2024
© A.R. Lowry 2008-2024
Read for Mon 29 Jan: Burger 65-81 (Ch 3-3.2)
Fermat’s Principal & Snell’s Law:
• Fermat’s principle (the propagation path or raypath is
always the path requiring least time) leads to Snell’s
Law :
Snell’s law predicts (for example) that a ray entering a slower
medium bends away from the boundary
• Reflections & Refractions: A wave traveling across a
boundary conserves energy ; has continuous stress
& displacement  reflects some energy, transmits some
energy, and often converts some energy to another
phase (e.g. P to S).
• All are governed by Snell’s Law!
Here, q is the angle of incidence between the raypath and the normal to a boundary separating two media (1, 2) with different velocities V1 and V2

## Slide 2
Last time continued:
• The Critical Angle is the angle of incidence for which the
refraction parallels the interface:
(& at > angles, no refraction!)
• Diffractions occur at “scatterers” or non-ideal
boundaries; are predicted by Huygen’s Principle but not by
ray theory/Snell’s Law.

## Slide 3
Some basic concepts of seismic amplitude:
Impedance Contrast:
Thus far we’ve focused much of the discussion on concepts
related to velocity & travel-time, but seismic waves also have
amplitude, A, of the particle displacements:
incoming P
A
Amplitudes of reflections &
refractions are determined by
energy partitioning at the
boundary. A normally-incident (= 0)
P-wave with amplitude Ai produces a
reflected P-wave with amplitude:
q
(reflection
coefficient)
and a refracted P:
where Zi = iVi is the impedance in layer i
(refraction
coefficient)

## Slide 4
Important to note:
Many seismology methods focus on travel-time &
hence are parameterized by velocity (e.g., tomography,
the refraction method, …). Reflection seismic uses
amplitude so it responds to impedance!
2. The relations for reflection get much more complicated
when   0. We will introduce Zoeppritz’ equations
for the non-trivial case later…

## Slide 5
Source Amplitudes relate to the initial energy
released by the source and the coupling of the source
to the medium:
In addition to energy partitioning at impedance boundaries,
seismic amplitudes depend on geometrical spreading,
absorption attenuation & source amplitude:

## Slide 6
In addition to energy partitioning at impedance boundaries,
seismic amplitudes depend on geometrical spreading,
absorption attenuation & source amplitude:
Spherical spreading is
the redistribution of constant
energy in expanding volume:
Strain energy (per unit area)
averaged over one period or
wavelength is (e.g., for an
S-wave):
Area of the wavefront is 2 r2
so
r0 = 1
A = A0
r = 2
A = A0/2

## Slide 7
Consider a head wave (or “critically refracted” wave):
Area of the wavefront is cylindrical rather than a half-sphere
so increases proportional to 2 r instead of 2 r2 for a half-sphere
Hence cylindrical spreading

## Slide 8
Anelastic Attenuation or Absorption:
Geometrical spreading assumes a perfectly elastic medium
in which there is no conversion of strain energy to other
forms. However observation  most Earth media are
dissipative (energy is lost to work— anelastic strain—
and ends up converted to heat).
For a plane wave, the Amplitude A decreases as
where a is the absorption coefficient, a = f/QV = /2QV
Q is generally called Quality factor… High Q implies
low attenuation.

## Slide 9
So amplitude gets smaller with greater distance traveled x and
higher frequency f ; remains larger when intrinsic quality
factor Q and velocity V are higher.
Q differs for P-waves (Qp) and S-waves (Qs).
For sediments,
5 < Qp < 300 (lower if porosity is high)
5 < Qs < 100
For crystalline rocks,
100 < Qp < 800
Example: Pierre shale Qp = 20, Vp = 2100 m/s
How far until a 30 Hz plane wave is 10% of original amplitude?
ln(0.1) = – (30 Hz) / 20 (2100 m/s)  ~ 1000 m