## Slide 1
Geology 5660/6660
Applied Geophysics
31 Jan 2024
© A.R. Lowry 2008-2024
Read for Fri 2 Feb: Burger 81-105 (Ch 3.3-3.6)
Last time: Seismic Amplitudes
• Attenuation quality factor Q is another physical rock property
that gives different information than velocity (more sensitive
to shallow porosity & fluids, deep temperature, melt & volatiles)
• Q is hard to measure though because amplitudes also depend
on energy partitioning (i.e., mode conversions),
multipathing, and scattering
• Still, Q can help to interpret seismic images (if you can measure
it)!

## Slide 2
Last time continued: Zoeppritz Equations
• Mode Conversion (P to S or S to P) occurs when  ≠ 0
• Introduced the ray parameter (based on Snell’s Law):
 Predicts propagation paths if ,  structure is known!
• Continuous displacements ( , ) and stresses
( , ) provide four equations in five unknown
amplitudes of incoming and outgoing waves… Normalize
by amplitude of incoming wave gives Zoeppritz’ equations
• Graphical user interface models of Zoeppritz’ equations are at
http://www.crewes.org/ResearchLinks/ExplorerPrograms/ZE/

## Slide 3
Four equations in five unknown amplitudes leaving a velocity
boundary are called Zoeppritz’ Equations.
If we fix the amplitude for the incident wave (e.g., A0 = 1),
we can solve for the other four algebraically.
Model from:
https://crewes.org/
ResearchLinks/
ExplorerPrograms/ZE/
1 = 2000, 2 = 2200
kg/m3
1 = 3000, 2 = 4000
m/s
1 = 1500, 2 = 2000
m/s
Rp
Tp
Rs
Ts
Crewes Zoeppritz Explorer
(T = “Transmitted”;
R = “Reflected”)

## Slide 4
water
shale
gas sand
shale
Example for
a synthetic
seismogram

## Slide 5
water
shale
gas sand
shale
Rp
Tp
Rs
Ts
Water/Shale
Shale/Gas Sand

## Slide 6
4D: imaging
changes in
impedance:
From Osdal
et al., The
Leading
Edge, 2006
2001-2003
2001-2004
Model
w/out
seismic
Model
with
seismic
Red = gas cap over oil (neutral colors); blue =  Z from injected water

## Slide 7
Amplitude versus offset (AVO) methods
give information about deep layers that you can’t get
from travel-times or reflection migration alone, and
are especially useful for evaluating fluid types &
pressures…

## Slide 8
The Refraction Method:
Recall first arriving seismic wave is the direct wave near
the source, and refracted (head) waves further out:
Problem:
We start knowing little
or nothing about the
subsurface, and our
objective is to use the
observations to
learn what’s under our
feet.

## Slide 9
V1
Consider the simple case of one horizontal layer over a
half-space with higher velocity:
Direct wave travels horizontally at velocity V1. On a plot of
time vs distance, arrivals are a straight line with
slope t/x = 1/V1 and intercept t = 0, i.e., t = x/V1.
Refracted wave travels horizontally at velocity V2 at the
top of layer 2, so a line with slope 1/V2. The intercept
now adds the time traveled in the first layer (& subtracts the
time not traveled in the second layer), i.e., t0 = 2a/V1–2b/V2.
This wave has incident angle ic = sin-1(V1/V2), so
Direct arrival
Refracted arrival
a
b
ic
h
V2
(Exercise)

## Slide 10
The mathematical
simplicity of finding
structure from slope &
intercept of a line made
refraction the tool of
choice in early imaging
studies!
So, can fit lines t = mi x + bi to the first arrival travel-times…
Then V1 = 1/m1 , V2 = 1/m2 , and
In the plot above, m1 = 0.001 s/m, m2 = 0.0002 s/m,
b2 = 0.0118 s. What are the velocities & depth?
(Exercise)