## Slide 1
© A.R. Lowry 2023
Geology 6690/7690
Geodesy & Crustal Deformation
15 Sep 2023
GPS/GNSS Positioning
• Resection (location of intersecting ranges, or
pseudoranges if we acknowledge receiver clock error,
to solve for x, y, z, Dt of the receiver)
• Involves three components:
i. Space segment (satellite vehicles  active
transmission)
ii. Control segment (orbit determination &
communication)
iii. User segment (antenna/receiver  passive)
Read for Mon 18 Sep: Wahr §3.1-3.2 (67-75)

## Slide 2
Last time(s) continued!
Critical Thinking when reading papers
• Understand the terminology & conceptual framework
• Carefully consider observations: What’s relevant? What else
is in there? How do you separate the two?
• Examine the data analysis. Are there better ways quantify,
observations, extract desired signal, or remove other signals?
• Examine the modeling methodology (including boundary/initial
conditions, modeling assumptions, process/property
assumptions)…

## Slide 3
GPS Signal Structure
Cesium clocks on SV’s have fundamental frequency
f0 = 10.23 MHz (offset by 0.44647 mHz for relativistic
effects between SV and surface)
Clocks are stable to 10-13 s/day (= 0.03 mm range)
Cesium oscillator drives both signals and codes:
Signals are unmodulated carrier frequencies Li = ai cos(fit)
(Recall f = 2p/T = c/l)
L1  154f0 = 1575.42 MHz wavelength  = 19.0 cm
L2  120f0 = 1227.60 MHz wavelength = 22.4 cm
(Also L3 for communicating nuclear detonation detection data;
L4 (add’l ion corr); L5  115f0 = 1176.45 MHz in preparation for
a civilian Safety of Life/Search and Rescue comm channel)

## Slide 4
GPS Signal Structure
Carrier frequencies are modulated (multiplied) by +1 or –1
using binary codes:
C/A (Coarse Acquisition) code  fo/10 = 1.023 MHz
(l = 293 m)
– Unique, public pseudo-random noise code for each SV
– PRN code repeats once per millisecond
– Receivers use known PRN to cross-correlate with
antenna-measured microwave signal and pull out
individual SV signals!
+1
–1
1
1
1
1
0
0
0
“chips”

## Slide 5
GPS Signal Structure
Other codes include:
P (Precise) code f0 = 10.23 MHz (l = 29.3 m)
– Unique ENCRYPTED PRN for each SV (Also called
Y-code); an anti-spoofing (AS) measure intended to
ensure selective availability; prevent jamming
– PRN would repeat once every 266.4 days!
BUT the key is changed once per day…
Message code at 50 Hz contains:
–satellite health
–almanac (approx. orbits = first 6 of 21 ephemerides)
–satellite clock correction term
–time tag
• More recently, CM & CL codes for civilian navigation;
CNAV for more sophisticated navigation messaging;
M-Code: Military-only (anti-jamming & secure access)

## Slide 6
GPS Signal Structure
Codes are applied to signals in quadrature as:
L1 = a1P(t)M(t) cos(f1t) + a1C/A(t)M(t) sin(f1t)
L2 = a2P(t)M(t) cos(f2t) (*Note: Now have 23 “L2c” SVs!)
EXAMPLE: To get a code range rC/A, the receiver
cross-correlates known C/A PRN with signal at
L1 frequency to get a time shift:
1 1 0 1 0 1 0 1 1 0 0
1 1 0 1 0 1 0 1 1 0 0
Dt plus Message time tag gives “pseudorange”
R = cDt = rC/A + cd
(Error in a standard receiver quartz clock ~ 10-5 s = 3000 m!)
Need a minimum four pseudoranges R to calculate X, Y, Z, d
Dt

## Slide 7
For Tectonic Geodesy…
Tectonic and other high precision geodesy uses specialized
instruments that use L2c and/or:
Cross-correlate L1 quadrature and L2 signal to extract P-code
Track phase  of the L1 and L2 carrier frequencies
Then perform specialized post-processing of phase (and
sometimes code) data, with specially post-processed
orbits and clocks, to model out most sources of error in
ranges. We then average the position estimates over a long
period (e.g. 1 day)…
Current processing methods can achieve repeatability of
daily horizontal positions <1 mm!

## Slide 8
Note: Tracking phase F of the carrier
frequencies means that we are really
measuring the change in range,
over time, from the satellite to the
receiver (called the doppler)
This means the actual range r at any
given time t is unknown; instead it
must be solved for from the known
satellite orbits and the doppler
measurements F(t)
Knowing the initial range r0 at time t0
(plus the doppler) is enough to know
the range at all other times. We
call this unknown/solved for initial
range the ambiguity
SV1
SV1
SV1
t0, r0, F0 = 0
t1, r1, F1
t2, r2, F2

## Slide 9
Positions from L1-C/A
code ranges only
are used in (cheap)
handheld or phone
GPS. Errors are of
order 10’s of m! Much
too large for our purposes.
These repeat positions used tectonic-grade
instruments recording
both code and phase!
Differences reflect errors in orbits/clocks
of the real-time Nav
message and ambiguity errors…

## Slide 10
GPS Error Sources (and Mitigation)
Satellite position and SV clocks:
Real-time (Nav Message) orbit
plus clock drift errors ~ 5 m
Various orbit estimation centers
(e.g., IGS, JPL) solve for satellite
position, velocity, clocks and
provide to users (error ~ 3-6 cm)
Network positioning applications
remove these common mode
errors by differencing
• Precise point positioning does not
difference; neglects these errors
Dra b
Single Difference Correction
Double Difference Residual
a –2a – r1b + r2b
A
B
A
B
1
2
(yields an ambiguity that’s
an integer # of wavelengths)