## Slide 1
Geology 6600/7600
Signal Analysis
21 Sep 2017
© A.R. Lowry 2017
Last time:
• The average power of a random process x is
• The Cross-Power Spectrum relating two random
processes x and y is given by:
and has the property . Generally the
cross-power spectrum will be complex-valued (i.e., it will
contain phase as well as amplitude information).
• The Coherence Function is defined as:
and ranges from zero (uncorrelated
processes) to one.
• The spectrum of the sum of two random processes is
~
~
~

## Slide 2
Linear Systems with Stochastic Inputs:
Signal analysis has a long list of applications in systems
engineering, electrical engineering, etc. (with signals
including sound, images, telecommunications).
Consider for example a deterministic signal (i.e., a
signal f for which f(t) is fixed and can be determined at
every t from some mathematical expression) that has
finite energy:
For example, power dissipated in a  resistor is P = I 2R = I 2.
Energy relates to power as

## Slide 3
Consider the energy in the frequency domain ():
Notation convention: we will denote the Fourier
transform of a (lower-case letter) function or process by
an (upper-case letter) amplitude.
If we let  so that
and if f(t) is real F() = F*(–) (exer: Use )
then:

## Slide 4
This gives us Parseval’s Relation:
This is the Energy Density for . More generally, for
a signal x:
is the Energy Density Spectrum.
The integral of energy in a particular frequency band [1,2]
is the Power Spectral Density over that frequency
band.

## Slide 5
A Linear System is any system for which an output
signal y(t) represents a convolution of the system’s
“impulse response” (or “system function”) h(t)
with an input x(t).
Then if the input and system functions are known, the
output can be found by:
1) y(t) = h(t)  x(t)
2) Y() = H()X()
From 2), we can get |Y()|2 = |H()X()|2 = |H()|2|X()|2
and the energy density spectrum is:
x(t)
h(t)
y(t)

## Slide 6
Autocorrelation for a (deterministic) finite-energy signal:
has properties:
(similar to those for random processes).
Cross-correlation:
Correlation Theorem:
Note the primary difference from random processes is that
we can integrate over ±∞ for expectation operator E{•}!

## Slide 7
From these relations we have two ways to find an energy
density spectrum:
Exercise: find the energy spectrum of a pulse function
x(t) = APT(t) in two different ways:
t
x
T/2
–T/2

## Slide 8
Random Signals: (Finite Power; Infinite Energy)
Consider a linear system with a random process input x(t)
and impulse response h(t):
In this instance, the output y(t) will also be a random process
corresponding to the convolution:
If this is a (time-domain) causal system, that’s equivalent
to integrating from t = 0 to ∞, as h(t) = 0 for t < 0.
~
~

## Slide 9
The cross-correlation of the input and output from a SISO
linear system is now:
So:
is the convolution of the autocorrelation of the input with the
impulse response,
The autocorrelation of the output signal is:

## Slide 10
We may recall from properties of the cross- and auto-
correlations:
Thus:
Consider for example a zero-mean, white noise input:
The delta function is even, so ––:
(Let –):

## Slide 11
The output variance for the system is:
By Parseval’s relation,
i.e., the output variance is the input variance multiplied by
the energy spectral density of the impulse response!

## Slide 12
Recall from earlier the transform relations:
(autocorrelation) (autopower spectrum)
(crosscorrelation) (crosspower spectrum)
Then we can also express the autocorrelation & autopower
spectrum of the output signal as:
Note the output autopower has no phase information, so cannot
be used to fully characterize the system h(t)!

## Slide 13
Example: Consider the low-pass filter h(t) = e–at u(t)
(Can get this e.g. from a resistor/capacitor circuit):
h(t)
t
u(t)
t
1
1
Here, given direct current I get
voltages (in the frequency
domain):
for a = 1/RC
R
x(t)
C
y(t)
~
~

## Slide 14
The modulus-squared of H is then:
Let’s assume we have a zero-mean, white noise input to the
circuit:
Then:
Variance of the output will be:
S0
Input spectrum:
S0
Output spectrum:

## Slide 15
Examples of correlation functions & power spectra:
Random sine wave
Autocorrelation:

Power Spectrum:
t
x
t
R

S



## Slide 16
Examples of correlation functions & power spectra:
White noise with zero mean, variance :
Autocorrelation:

Power Spectrum:
t
x
t
R

S

## Slide 17
Examples of correlation functions & power spectra:
Low-pass filter (i.e. applied in the frequency domain):
Band-Pass filter (in the frequency domain):
Autocorrelation:

Power Spectrum:
t
R

S
Autocorrelation:

Power Spectrum:
t
R

S




(sinc fn!)

## Slide 18
Examples of correlation functions & power spectra:
Pseudo-random Binary Sequence (PRBS):
Markov Process (may be useful to describe noise in
potential field data):
Autocorrelation:

Power Spectrum:
t
R

S
Autocorrelation:

Power Spectrum:
t
R

S
t
x
“Similar” to white noise, but not, because it’s deterministic