## Slide 1
Geology 6600/7600
Signal Analysis
31 Oct 2017
© A.R. Lowry 2017
Last time: Linear Systems
• Uncorrelated additive noise in the output signal, y = v + n, of
a SISO system can be estimated for power spectra by
recognizing that Sxy = Sxv and Syy = Svv + Snn so
• When noise is present in both the input and output signals,
can bound the true response & signal-to-noise ratios:
Lo-bound: Hi-bound:
• Multiple frequency responses in a linear MISO system can be
estimated from the system of linear equations:
(ill-determined for strongly correlated inputs…)

## Slide 2
Geology 6600/7600
Signal Analysis
Last time continued: Linear Systems
• The Multiple Coherence Function measures coherence
of combined inputs to output:
giving it similar utility to the SISO coherence in characterizing
additive noise that is unrelated to the measured inputs!

## Slide 3
Reading for Tuesday (7 Nov):
Becker, T.W., et al., Static and dynamic support of western
United States topography, Earth Planet. Sci. Lett., 2014.
(I will prep discussion materials… You’ll need to
be prepared to discuss specifically the
SIGNAL ANALYSIS methods used in the paper!)
Two “background” items to discuss:
• An early draft examined only global cross-correlations, but
an associate editor wanted to see wavelength-dependence
of cross-correlation. How was this addressed, and how
does that approach relate to other topics in this class?
• The associate editor asked whether the revised approach
acts as a zero-phase filter in the frequency domain. How
could you test this?

## Slide 4
Digital Wiener Filtering:
Suppose we have the linear SISO digital system:
And we would like to design an “optimum h” so that
, some “desired” output. Possible applications
for such a transfer function might include:
(1) Smoothing:
where s[n] is desired signal and v[n] is
uncorrelated noise, in which case:
(2) Prediction:
~
~

## Slide 5
To accomplish our goal, we will seek to find the h that
minimizes the mean-squared error (MSE):
for all m.
That is, we want to set the error
orthogonal to the input signal!
The Orthogonality Principle (as commonly applied in
linear estimation theory) states that the error vector of the
optimal estimator (in a mean square error sense) is
orthogonal to any possible estimator.
Expanding:
Thus or

## Slide 6
So, our time domain solution is:
Obviously if we “know” Rxd a priori, this problem can be solved
in the frequency domain, where for  = t:
But in the time-domain, the 2N + 1 length filter, expanding via
the Yule-Walker equations, can be written:
for all n = –N, –N+1, …, 0, 1, …, N
This system of linear equations can be written in matrix form:
for which output would then be:

## Slide 7
So now let’s briefly return to our applications mentioned
earlier:
(1) Smoothing: where s[n] is desired
signal and v[n] is uncorrelated noise.
Recall that Rsx[m] = Rxx[m]h[m] in the time domain,
while in the frequency domain

## Slide 8
As a reminder, we can inverse Fourier transform spectra
to correlation functions and write out the expectation
operators to show that:
and
If we assume that s and v are uncorrelated then:
Note, however, that this approach assumes a priori
that we know something independently about the
statistics of the “noise” signal, or the statistics of the
desired signal, or both! Recall the general knock on
“Bayesian” approaches…
~
~